     Network Configuration and pfodApp Instructions

This Dual pfod Controlled Power Switch can be connected to your Wifi Network
using pfodWifiConfigV1.
1. Install pfodWifiConfigV1 from GooglePlay or SlideMe on your Android mobile
2. Unplug all leads from this Power Switch
3. Start pfodWifiConfigV1 and scan the QR code above.
4. Hold down both push buttons and plug in the black power lead and turn on.
5. Both push buttons will flash for 10 secs and then the Power Switch will be config mode.
6. When the configuration screen shows on your mobile,
   enter your Wifi network name and password and
   the IP address and portNo for this Power Switch
7. Turn the power on and off again when finished to connect the Power Switch
   to your network.
8. To control this Power Switch with pfodApp, create a new connection and enter the
   IP address and portNo set above. For the password scan the QR code above.
   Save the connection.
        Currently Configured IP:port setting is 10.1.1.102:4989